## Slide 1
Renesas RA6M5 cloud kit workshop
Introduction – Live demo – Hands on
April 2023
Duy Nguyen
RVC/IIBU/SDD/SWD/FSP1
Renesas Electronics Corporation

## Slide 2: Agenda
Introduction RA6M5 Cloud Kit Page 03
Development environment Page 08
Demo and Hands-on Page 19
      Demo Cloud application (Ethernet)
      Demo create project Blinky (hands-on)
      Demo print data to tera-term using UART (hands-on)
      Demo read Data from HS3001 sensor (hands-on)
      Demo Read Data from external SENSOR using i2c (adxl345)
      Read Data from external SENSOR using SPI (MAX31722)
Q&A Page 98

## Slide 3: Introduction RA6M5 Cloud Kit RA series and application Examples
Renesas RA Family MCU Portfolio
From RA ARM Cortex-M 32-bit MCUs, Cortex-M33, M23 and M4 | Renesas
From: https://www.renesas.com/us/en/document/bro/renesas-ra-family-brochure?r=467666
Application Examples

## Slide 4: Introduction RA6M5 Cloud Kit Renesas RA Microcontroller Kits
From Renesas RA Microcontroller Evaluation Kits, Embedded & IOT Kits | Renesas
Training & Video:
Beginner's Guide: Official Renesas RA Family Beginner's Guide | Renesas
Videos: Renesas RA Family Video Library | Renesas
Target of today introduction CK-RA6M5 - Cloud Kit Based on RA6M5 MCU Group | Renesas

## Slide 5: Introduction RA6M5 Cloud Kit CK-RA6M5
  CK-RA6M5 is a cloud kit base on RA6M5 MCU Group
  It’s aim to provide a simplify way for the process of IoT solution prototyping
  RA 32-bit MCUs:
    High efficiency
    Advanced security
    Flexible Software Package
Target Applications
  Home and Building
  Automation
  Smart Cities
  Healthcare
  Industrial Monitoring
  Voice Command
  Smart Metering
  Asset Tracking and Location Based Service

## Slide 6: Introduction RA6M5 Cloud Kit CK-RA6M5

## Slide 7: Introduction RA6M5 Cloud Kit CK-RA6M5
Arduino form factor
2 PMOD connector
Sensors:
Temperature/Humidity
Barometric pressure
Indoor AQI
Outdoor AQI
Biometric sensor
9-Axis MEMS IMU
2 MEMS microphones
3 User LEDs-red, green, blue
USB
Debug
Host
UART serial terminal
RA6M5 MCU
Ethernet
RYZ014A Pmod CAT-M1

## Slide 8
Development environment

## Slide 9: Development environment Flexible software package (FSP) - Introduction
  Renesas Flexible Software Package (FSP) is an optimized software package designed to provide easy to use, scalable, high-quality software for embedded system design. The primary goal is to provide lightweight, efficient drivers that meet common use cases in embedded systems.
  FSP is consist of:
    Driver for almost peripheral on Renesas MCU
    FreeRTOS (AWS) / Azure RTOS (Microsoft)
    Arm Mbed TLS, Mbed Crypto, & LittleFS/ Azure RTOS FileX
    SEGGER emWin & TES Dave2D
From: Official Renesas RA Family Beginner's Guide
The different layers of the Flexible Software Package and their functionality

## Slide 10: Development environment Flexible software package (FSP) – Common terminology
Module
Modules can be peripheral drivers, purely software (middleware), or anything in between.
Modules are the core building block of FSP. Modules can do many different things, but all modules share the basic concept of providing functionality upwards and requiring functionality from below.
Stack
When modules are layered atop one another, an FSP stack is formed.
Application
FSP Module
BSP
Module
Provides
Requires

## Slide 11: Development environment Flexible software package (FSP) – Common terminology
Interface: I2C master
r_i2c_master_api.h
Peripheral: SCI
Module: r_sci_i2c
Peripheral: IIC
Module: r_riic
inc
fsp
api
r_i2c_master_api.h
instances
r_iic_master.h
src
r_iic_master
r_iic_master.c
Almost FSP module will have source structure similar like this.
I2C master interface with 2 different modules
Source code structure

## Slide 12: Development environment Flexible software package (FSP)
Interface
At the architecture level, interfaces are the way that modules provide common features
Interfaces aim to provide support for the common features that most users would expect
FSP interface consist of:
  FSP Interface Enumerations
  FSP Interface Callback Functions
  FSP Interface Configuration Structure
  FSP Interface API Structure
  FSP Instance Control Structure

## Slide 13: Development environment Flexible software package (FSP)
Instance
While interfaces dictate the features that are provided, instances actually implement those features
FSP instance consist of:
  FSP Instance Control Structure
  FSP Interface Extensions
  FSP Instance API

## Slide 14: Development environment Flexible software package (FSP)
FSP for RA is currently supported on 3 IDE:
e2studio (GCC for ARM)
Keil C (ARM Compiler)
IAR (IAR Compiler)
Target for today session

## Slide 15: Development environment Flexible software package (FSP)
FSP releases: Releases · renesas/fsp (github.com)
FSP package only
Include e2studio + FSP package

## Slide 16: Development environment How to install
For user doesn’t have e2studio install on the PC yet.
Open the file setup_fsp_v4_2_0_e2s_v2022-10.exe and choose “All user”
The installation window will popup choose Quick Install and click Next.

## Slide 17: Development environment How to install
For user doesn’t have e2studio install on the PC yet.
Installer application will check and list out what needed to be install. Click Next
Read License Terms and Conditions => Choose Accept the terms and Click Install.

## Slide 18: Development environment How to update FSP version with existing e2studio
For user already have e2studio install on the PC yet and want to update FSP version:
Open FSP_Packs_v4.2.0.exe, installer window will pop-up, click “Next”
Read License Terms and Conditions and click “I Agree”.
Browse to folder where e2studio is installed and click “Install”

## Slide 19
Demo and Hand-ons

## Slide 20: Demo and HandS-on
      Demo Cloud applications
      Demo create project Blinky (hand-on)
      Demo print data to teraterm using UART (hand-on)
      Demo read Data from HS3001 sensor (hand-on)
      Demo Read Data from external SENSOR using i2c (adxl345)
      Read Data from external SENSOR using SPI (MAX31722)

## Slide 21: Demo and HandS-on
      Demo Cloud applications
      Demo create project Blinky (hand-on)
      Demo print data to teraterm using UART (hand-on)
      Demo read Data from HS3001 sensor (hand-on)
      Demo Read Data from external SENSOR using i2c (adxl345)
      Read Data from external SENSOR using SPI (MAX31722)

## Slide 22: List of Current cloud Applications
Currently, there are 3 reference cloud applications which were public in Renesas website
AWS + Ethernet: RA AWS MQTT/TLS Cloud Connectivity Solution – Ethernet Application Project (renesas.com)
  Sample Code: https://www.renesas.com/in/en/document/scd/ra-aws-mqtttls-cloud-connectivity-solution-ethernet-application-project?language=en&r=1611751
AWS + Cellular: RA AWS MQTT/TLS Cloud Connectivity Solution – Cellular Application Project (renesas.com)
  Sample Code: https://www.renesas.com/in/en/document/scd/ra-aws-mqtttls-cloud-connectivity-solution-cellular-application-project?language=en&r=1611751
Azure + Ethernet: RA AWS MQTT/TLS Cloud Connectivity Solution – Ethernet (renesas.com)
  Sample Code: https://www.renesas.com/in/en/document/scd/ra-aws-mqtttls-cloud-connectivity-solution-ethernet?language=en&r=1611751

## Slide 23
CK-RA6M5 Setup

## Slide 24: Connecting and Powering Up the CK-RA6M5 Board
Check that:
    A. J22 is set to link pins 2-3
    B. J21 link is closed
    C. J16 Link is open
2. Connect J14 and J20 on the CK-RA6M5 board to USB ports on the host PC using the 2 micro-USB cables supplied.
3. Power LED (LED6) on the CK-RA6M5 board lights up white, indicating that the CK-RA6M5 board is powered on.

## Slide 25: A. J22 is set to link pins 2-3
J22 is set to link pins 2-3

## Slide 26: B. J21 link is closed
J21 link is closed

## Slide 27: C. J16 Link is open
J16 Link is open

## Slide 28: Power LED (LED6) on the CK-RA6M5 board lights up white
3. Power LED (LED6) on the CK-RA6M5 board lights up white, indicating that the CK-RA6M5 board is powered on.

## Slide 29: Download Ethernet application of CK-RA6M5
Download from: https://www.renesas.com/in/en/document/scd/ra-aws-mqtttls-cloud-connectivity-solution-ethernet-application-project?language=en&r=1611751

## Slide 30: Import Ethernet application of CK-RA6M5
Notice: Current application use FSPv4.2.0, should refer to guideline how to change FSP version in E2studio before import

## Slide 31: Confirm FSP version
Generate Project when version is correct

## Slide 32: build and debug to board
Success

## Slide 33: build and debug to board
Push resume to load image to board
Push until status is running then push to stop

## Slide 34: Running Example Project (1/5)
On the host PC, open Windows Device Manager. Expand Ports (COM & LPT), locate USB Serial Device (COMxx) and note down the COM port number for reference in the next step.

## Slide 35: Running Example Project (2/5)
Open Tera Term, select Serial and COMxx: USB Serial Device (COMxx) and click OK.

## Slide 36: Running Example Project (3/5)
Using the Setup menu pull-down, select Serial port… and ensure that the Baud rate is set to 115200, data is set to 8 bit, parity is set to none, and stop is set to 1 bit, as shown below.

## Slide 37: Running Example Project (4/5)
Complete the connection. The ‘welcome and main menu’ screen will be displayed.

## Slide 38: Running Example Project (5/5)
Press 3 to display the MCU ID (UUID). Copy the UUID for registration in dashboard.

## Slide 39
Cloud Kit Registration and Access to Dashboard

## Slide 40: Cloud Kit Registration and Access to Dashboard (1/8)
Sign up at https://www.renesas.cloud-ra-rx.com/ with an email that was not used previously for signing up for an AWS account.

## Slide 41: Cloud Kit Registration and Access to Dashboard (2/8)
Enter your first name, last name, email address and password and press on the button Register. You are redirected to Confirm your email page.

## Slide 42: Cloud Kit Registration and Access to Dashboard (3/8)
Verification code will be sent to your email. Enter the code and press on the Send button. You are redirected to Register Device page.

## Slide 43: Cloud Kit Registration and Access to Dashboard (4/8)
Enter the UUID of the kit to complete the registration process. UUID is the unique ID of your board. In previous steps we obtain the UUID of the kit from TeraTerm.

## Slide 44: Cloud Kit Registration and Access to Dashboard (5/8)
The registration page indicates that the device registration is in progress.

## Slide 45: Cloud Kit Registration and Access to Dashboard (6/8)
Wait for the ‘Invitation to join AWS Single sign-on’ email to activate the account. It could take up to 10 min to receive this email. Accept the invitation. Note that this invitation will expire in 7 days. If your invitation expires, please contact Renesas support.
On accepting the invitation, you will be redirected to the AWS Sign up page.
If you choose to sign into your AWS account (the account indicated in the AWS invitation), enter your new password, and confirm to complete the Sign in process in AWS. You will be redirected to the Single Sign-On page.
Proceed to check the status of Renesas dashboard at https://www.renesas.cloud-ra-rx.com/login .

## Slide 46: Cloud Kit Registration and Access to Dashboard (7/8)
Wait for the Download Certificate and Go To Dashboard buttons to become available on the registration page. It may take up to 1 hour for the device provisioning process to complete.
Click Download Certificate button to download the credentials for connecting to the cloud.

## Slide 47: Cloud Kit Registration and Access to Dashboard (8/8)
Click go to Dashboard button to access the dashboard. First time users will access the dashboard with credentials “admin” for both username and password. Then, users will be directed to change the password. Once completed, users can access the dashboard.

## Slide 48
Setup certificate

## Slide 49: Setup certificate (1/11)
Back to main menu and press 2 to access Data flash.

## Slide 50: Setup certificate (2/11)
Update from “b)” to “e)” based on Certificate downloaded from dashboard.

## Slide 51: Setup certificate (3/11)
There are 4 files in cert folder.
Below is the files available in the folder.
Certificate
Private Key
MQTT Broker end point
IOT Thing name

## Slide 52: Setup certificate (4/11)
Update “b)”: File -> Send file.. -> Choose certificate.pem.crt

## Slide 53: Setup certificate (5/11)
Update “b)”: Successfully

## Slide 54: Setup certificate (6/11)
Update “c)”: File -> Send file.. -> Choose private.pem.key

## Slide 55: Setup certificate (7/11)
Update “c)”: Successfully

## Slide 56: Setup certificate (8/11)
Update “d)”: copy IOTEndPoint from iot-data.json (use Edit -> Past<CR>)

## Slide 57: Setup certificate (9/11)
Update “d)”: copy IOTEndPoint from iot-data.json (use Edit -> Paste<CR>)

## Slide 58: Setup certificate (10/11)
Update “e)”: copy IOTThingName from iot-data.json (use Edit -> Paste<CR>)

## Slide 59: Setup certificate (11/11)
Can check written information by “f)”

## Slide 60
Start AWS + Ethernet application

## Slide 61: Start AWS + Ethernet application
AWS + Ethernet loaded on board, reset board by S1 (Red button) to start for application
Choose “4” to start for application
Data from board will be publish on AWS and can be view on dash board.

## Slide 62
Hands-on

## Slide 63: Demo and HandS-on
      Demo Cloud applications
      Demo create project Blinky (hand-on)
      Demo print data to teraterm using UART (hand-on)
      Demo read Data from HS3001 sensor (hand-on)
      Demo Read Data from external SENSOR using i2c (adxl345)
      Read Data from external SENSOR using SPI (MAX31722)

## Slide 64: Demo and Hands on Blinky demo
Open e2studio and choose the path to create workspace.

## Slide 65: Demo and Hands on Blinky demo
Go to “File -> New -> Renesas C/C++ Project -> Renesas RA” to create new project for RA MCU

## Slide 66: Demo and Hands on Blinky demo
At this point project creation window will pop-up.
Click Next and enter project name as “CKRA6M5_demo”

## Slide 67: Demo and Hands on Blinky demo
In the next window choose FSP Version and CK-RA6M5 as target board, for this session I will use FSP v4.2.0.

## Slide 68: Demo and Hands on Blinky demo
In the next window choose “Flat (Non-Trustzone) Project”

## Slide 69: Demo and Hands on Blinky demo
Choose Build Artifact Select as “Executable” and RTOS Selection as No RTOS

## Slide 70: Demo and Hands on Blinky demo
In Project Template Selection window choose “Bare Metal – Blinky” to create an LED blinky project

## Slide 71: Demo and Hands on Blinky demo
After finished create project you will be asked by e2studio to open “FSP configuration perspective” => Click on Open perspective
Notes: Briefly describe FSP configuration window

## Slide 72: Demo and Hands on Blinky demo
Because on CK-RA6M5 external oscillation crystal is not solder in so we need to configure PLL source clock to use internal clock by go to “Clocks” tab in the FSP configuration window and choose “PLL Src: HOCO” like the picture below

## Slide 73: Demo and Hands on Blinky demo
Press “Generate Project Content” to generate the configuration for FSP

## Slide 74: Demo and Hands on Blinky demo
For Blinky project, source code for blinking LED on board is generated automatically in “hal_entry.c” file when create project, to build project right click on project and choose “Build project” or press “Ctrl + B”.

## Slide 75: Demo and Hands on Blinky demo
To load the build image into board we need to connect CKRA6M5 debug port into PC using USB cable provided in the kit. Right click on project choose “Debug As -> 4 Renesas GDB Hardware Debugging”
    Then click on “Resume” icon to start the code.

## Slide 76: Demo and Hands on Blinky demo
Result is the LED on board will blink
Notes: Show debug perspective

## Slide 77: Note for Clock

## Slide 78: Note for FSPv4.3.0

## Slide 79: Demo and HandS-on
      Demo Cloud applications
      Demo create project Blinky (hand-on)
      Demo print data to teraterm using UART (hand-on)
      Demo read Data from HS3001 sensor (hand-on)
      Demo Read Data from external SENSOR using i2c (adxl345)
      Read Data from external SENSOR using SPI (MAX31722)

## Slide 80: Demo and Hands on Print data to teraterm using UART
For this demo we will need to check CKRA6M5 Schematic document
In the same project open FSP configuration file and switch to tab “Stacks”
Notes: Open Renesas Official web and show where to download the Schematic package:

## Slide 81: Demo and Hands on Print data to teraterm using UART
To add new UART module click on “New Stack -> Connectivity -> UART (r_sci_uart)”

## Slide 82: Demo and Hands on Print data to teraterm using UART
Click on new UART stack to configure for it, because USB SER is connected to UART channel 5 on MCU so we will modify Channel to 5 by “Property -> Module g_uart0 UART (r_sci_uart) -> General -> Channel -> 5 ”.
Add callback function “user_uart_callback”

## Slide 83: Demo and Hands on Print data to teraterm using UART
Steps for coding in hal_entry.c:
Initialize UART instance.
Create callback function for UART instance.
Create console write function.
Trial print “Hello world!!”
Notes: Show reference example code on how to use UART on RA github io RA Flexible Software Package Documentation: Introduction (renesas.github.io) Show developer assist during code

## Slide 84: Demo and HandS-on
      Demo Cloud applications
      Demo create project Blinky (hand-on)
      Demo print data to teraterm using UART (hand-on)
      Demo read Data from HS3001 sensor (hand-on)
      Demo Read Data from external SENSOR using i2c (adxl345)
      Read Data from external SENSOR using SPI (MAX31722)

## Slide 85: Demo and Hands on Read Data from HS3001 sensor
For this demo we will need to check CKRA6M5 Schematic document
In the same project open FSP configuration file and switch to tab “Stacks” .
Click on “New Stack -> Sensor -> (rm_hs_hs300x)”.
Notes: Open Renesas Official web and show where to download the Schematic package:

## Slide 86: Demo and Hands on Read Data from HS3001 sensor
Click on Add I2C Communications Peripheral to add I2C interface, “New -> I2C Master (r_iic_master)”

## Slide 87: Demo and Hands on Read Data from HS3001 sensor
Steps for coding in hal_entry.c:
Open the I2C bus
Intialize HS300x sensor
Create callback function for HS300x instance.
Start measurement and read data from sensor
Print HS300x sensor Data
Notes: Show reference example code on how to use UART on RA github io RA Flexible Software Package Documentation: Introduction (renesas.github.io) Show developer assist during code

## Slide 88: Demo and HandS-on
      Demo Cloud applications
      Demo create project Blinky (hand-on)
      Demo print data to teraterm using UART (hand-on)
      Demo read Data from HS3001 sensor (hand-on)
      Demo Read Data from external sensor using i2c (adxl345)
      Read Data from external sensor using SPI (MAX31722)

## Slide 89: Demo and Hands on Read Data from external SENSOR using i2c (adxl345)
For this demo we will need to check CKRA6M5 Schematic document and ADXL345 datasheet
In the same project open FSP configuration file and switch to tab “Stacks” .
Click on “New Stack -> Conectivity -> rm_comms_i2c”.
Notes: Open Renesas Official web and show where to download the Schematic package

## Slide 90: Demo and Hands on Read Data from external SENSOR using i2c (adxl345)
Click on Add I2C Shared bus to add I2C interface, “New -> I2C Shared Bus (r_comms_i2c)”
Click on Add I2C Communications Peripheral to add I2C interface, “New -> I2C Master (r_iic_master)”

## Slide 91: Demo and Hands on Read Data from external SENSOR using i2c (adxl345)
Click on r_iic_master instance and config Channel to 1
Click on g_comms_i2c_device1 I2C Communication device (rm_comms_i2c), config slave address and add callback function

## Slide 92: Demo and Hands on Demo Read Data from external SENSOR using i2c (adxl345)
Steps for coding in hal_entry.c:
Open the I2C bus
Intialize I2C Comm instance
Create callback function for ADXL345 I2C instance.
Start measurement and read data from sensor using I2C write and read functions.
Print ADXL345 sensor Data
Notes: Show reference example code on how to use I2C comm on RA github io RA Flexible Software Package Documentation: Introduction (renesas.github.io) Show developer assist during code

## Slide 93: Demo and HandS-on
      Demo Cloud applications
      Demo create project Blinky (hand-on)
      Demo print data to teraterm using UART (hand-on)
      Demo read Data from HS3001 sensor (hand-on)
      Demo Read Data from external sensor using i2c (adxl345)
      Demo Read Data from external sensor using SPI (MAX31722)

## Slide 94: Demo and Hands on Read Data from external SENSOR using SPI (MAX31722)
For this demo we will need to check CKRA6M5 Schematic document and MAX31722 datasheet
In the same project open FSP configuration file and switch to tab “Stacks” .
Click on “New Stack -> Conectivity -> r_sci_spi”.
Notes: Open Renesas Official web and show where to download the Schematic package

## Slide 95: Demo and Hands on Read Data from external SENSOR using SPI (MAX31722)
Configure SPI module
Click on r_sci_spi, configure “Property -> Module -> Name” to g_MAX31722
“Property -> Module -> Clock Phase” to “Data sampling on even edge, data variation on odd edge”
Add callback function, Property -> Module -> Callback” to MAX31722_sensor_callback
“Property -> Module -> Bitrate” to 50000

## Slide 96: Demo and Hands on Read Data from external SENSOR using SPI (MAX31722)
Configure pin for SPI communication, switch to tab “Pins”.
“Peripherals -> Connectivity:SPI -> SPI1”, Configure Operation Mode to “Disabled”
Choose “Peripherals -> Connectivity:SCI -> SCI0” , Configure Operation Mode to “Simple SPI” and change to use Port 4
Choose “Ports -> P4 -> P413” Configure Module to “Output mode (Initial Low)”

## Slide 97: Demo and Hands on Read Data from external SENSOR using SPI (MAX31722)
Steps for coding in hal_entry.c:
Intialize SCI SPI module
Create Slave select assert and deassert macro.
Create callback function for MAX31722 SCI SPI instance.
Configure sensore using SCI SPI Write API
Read sensor data using SCI SPI Write Read API
Notes: Show reference example code on how to use SCI SPI on RA github io RA Flexible Software Package Documentation: Introduction (renesas.github.io) Show developer assist during code

## Slide 98
Q&A Session

## Slide 99
We are welcome to receive all your feedbacks about CK-RA6M5 and workshop
Please Scan me
THANK YOU!

## Slide 100
Renesas.com